## Slide 1: Savitribai Phule Pune University, Pune Amrutvahini College Of Engineering, Sangamner Department of E&TC Engineering A Presentation on
“Voice operated lift control system with safety”
Presented By
1. Bhoknal Gayatri Satish(Roll no.07) 2. Varpe Aditya Rajendra(Roll no.66) 3. Waman Onkar Uttam (Roll no.69) 4. Zanjare Shaileshumar Gangaram(Roll no.72)
Under the Guidance of
Prof. V. R. Aware

## Slide 2: Contents
Introduction
Need of project
Research motivation
Aim and objective of project
Literature Survey
Problem Statement
Block Diagram of Project
Circuit Diagram
Prototype images
Hardware & Software requirements
Description of Components
Flow chart
Detailed algorithm
Advantages
Limitation
Application
Conclusion
References

## Slide 3: Introduction
Physically challenged people face many problems every day. One of these challenges is the use of elevators in many buildings. They should be able to enjoy using the elevator easily.
To overcome this challenge for the them, we must focus on the following issues: Make sure the person is at the elevator door, get elevator there and ask person where to go and accordingly go to respective floor.
Speech is the superior personality of the human beings gifted by the nature. Speech helps to deliver the thoughts and messages between human. Speech recognition is the process of the computer recognizing human speech to generate a string of words or commands. Sometimes it is known as automatic speech recognition.
Speech recognition is becoming more perplexing and difficult task. The speech recognition research is focuses mainly on large vocabulary, continuous speech capabilities and speaker independence[3].
A voice-operated elevator system is proposed where the user’s input commands to control the movement of the elevator system are kept convenient for the users. The commands include voice input for the floor operations, directions, elevator car’s door operation, and a special command to call for emergency[4].

## Slide 4: Need Of Project
The visually challenged people cannot use the elevator easily. It is difficult to use the keypad if they cannot see it. Sometimes the keypad has Braille technique, but they will have hard time for locating its place. Even though they found the keypad, how can they know the number if they do not know Braille?
They always need help in elevators from someone to press the button for them and to tell them when the elevator cabin arrives. In case of emergency how they will act if there is no one with them to help . So voice-controlled elevator can be a very good option for this people.
One more drawback of the current lift is that it cannot tell on which floor the lift is stuck, nor the parameters like temperature of motor, fire detection inside the lift. But by using this voice operated lift we can solve all these problems.

## Slide 5: Research Motivation
Elevators are an integral part of modern urban infrastructure, providing vertical transportation for millions of people daily. While elevator technology has advanced significantly over the years, there are still areas that require improvement, particularly in terms of user convenience and safety.
As most of the physically challenged people find it difficult to operate the elevator. Also modern elevators lacks features such as voice recognition and also its connectivity with the internet for real-time parameters and controlling the elevator.
So we’ve found a solution on this, integrating voice recognition capabilities with the lift(elevator) for conveniently operate elevator with just some voice commands and also get feedback in audio format from the lift control system.
Also send all this info in real-time to the lcd screen.

## Slide 6
Design and development of a voice-controlled lift/elevator control system with enhanced security features for human-machine communication.
Aim of the Project:
1. To operate lift through voice commands with easy use for people with visual and
physical challenges.
2. To measure parameters like floor number, weight of the lift, fire detection,
temperature of motor, etc.
3. To give real time information of lift parameters on the lcd screen.
Objectives of the Project:

## Slide 7
SR.NO. | Title Of Research Paper | Author Name | Published Year | Proposed System
1 | Elevator Control Using Speech Recognition for People with Physical Disabilities[4] | Komal Mahajan, Riddhi Nahar, Dhanali Khairnar, Shrutika Kinge, Sujata Suryawanshi | 2021 | The research combines speech recognition technology with machine learning to make the elevator control equipment that can be controlled by voice. This system uses python based machine learning libraries with Raspberry pi 3B+. The word can be trained for more than hundreds of words.
Literature survey

## Slide 8
SR.NO. | Title Of Research Paper | Author Name | Published Year | Proposed System
2. | Voice Operated Intelligent Lift[5] | Rashmi P C, Amulya, A Karthik Shetty, Akshata, Dilip Kumar U K | 2019 | In this system the lift operates based on the input voice commands. In this project MATLAB coding is used for voice recognition and IR sensor is used for detecting the floors and stopping the motor rotation. The DC motor is used for controlling the lift. The microcontroller is programmed using Embedded C.
3. | Voice Based Lift Control[6] | Malim Huzaifa Salim, Sami Jaitapkar, Faki Ziyaan, Kazi Ibrahim | 2022 | This system accepts input by microphone, and taking the elevator to the destination accordingly.

## Slide 9
 |  |  |  | It uses raspberry pi and a speech API to communicate with cloud for the voice recognition.
4. | Implementation of Voice based Touchless Lift System[9] | B. Swathi, Akshay S Prathap, Aiswarya V Kumar, Ranjitha R, Raviteja Kaki | 2021 | This system uses Arduino Mega and Elechouse V3 Voice Recognition Module to correctly detect the command given by user, and uses servo motor to lift up and down the elevator, and a servo motor to open and close the doors of the elevator. For all this motors, it uses a relay driver circuit for driving the motors.

## Slide 10: Problem Statement
“To design and develop a voice-controlled lift/elevator control system with enhanced security features for human-machine communication”

## Slide 11: Block Diagram

## Slide 12: Circuit Diagram

## Slide 13: Prototype Images

## Slide 14: Hardware and Software Requirements
H/W requirements:
  Atmega 2560 microcontroller
  Transformer
  Bridge rectifier with dc supply
  Load cell with hx711 sensor
  Flame Sensor (YL 38)
  Temp sensor (ds18b20)
  Voice recognition module(V3)
  Push buttons
  IR sensors (IR-08H)
  Ultrasonic sensor (HC-SR04)
  16×2 Lcd display
  I2C serial interface adapter module
  Audio player module (APR33A3)
  Speaker
  Motor driver circuit (L293)
  DC motor
S/W requirements:
  Arduino IDE
  PCB wizard

## Slide 15: Description of Components
Transformer: Steps down the AC mains voltage to a suitable level for the rest of the system.
Specifications:
Input Voltage: 230 V AC
Output Voltage: 12 V AC
Output Current: 2 A
Mounting: Vertical mount type
Winding: Copper
Bridge rectifier with dc regulated supply: Converts the AC voltage from the transformer to DC. And removes pulsating DC by using a electrolytic capacitor.
Specifications:
Input Voltage: 12 V AC
Output Voltage: 12 V DC
Output Current: 2 A

## Slide 16
Voice recognition module(V3):
  Converts the user's spoken commands into an command number which is already stored in module. Voice Recognition Module product is a speaker-dependent voice recognition module.
  Users need to train the module first before let it recognizing any voice command.
  Specifications:
Support a maximum of 80 voice commands, with each voice 1500ms (one or two words speaking).
Maximum 7 voice commands effectively at the same time.
User-control General Pin Output.
Analog Interface: 3.5 mm mono-channel microphone connector + microphone pin interface.
Input supply voltage: 4.5 - 5.5 V DC
Current: 40 mA
Recognition accuracy: 99%
Protocol: UART/GPIO

## Slide 17
Atmega 2560 microcontroller[10]:
  The brain of the system, which controls all of the other components. The ATmega2560 is an 8-bit, low-power microcontroller that is based on the AVR-RISC architecture. It's commonly found in the Arduino Mega 2560 development board.
Specifications:
Input supply voltage: 7 - 12 V DC
54 digital input/output pins (of which 15 can be used as PWM outputs)
16 analog input pins
4 hardware serial ports
16 MHz crystal oscillator
USB connection
Power jack
Reset button
8 KB of SRAM
4 KB of EEPROM
256 KB of flash memory (of which 8 KB
is used for the bootloader)

## Slide 18
16x2 LCD display:
Displays the current floor number and other system information. A 16x2 LCD display can display 16 characters on 2 lines. The characters are white on a blue background. The display has a 5x7 pixel matrix for each character.
Specifications:
Display capacity: 16 characters x 2 rows
Display color: Blue backlit
Character size: 2.95 mm wide x 4.35 mm high
Current requirements: 2 mA @ 5 V DC
Voltage requirements: 5 VDC +/- 0.5V
Character pixels: 5 W x 7 H
Total pins: 16
Data pins: 8 (D0 to D7)

## Slide 19
I2C serial interface adapter module:
This LCD I2C adapter module is designed to fit directly below the standard 16x2 LCD display. Then through this module, the LCD can communicate through I2C protocol which requires only 2 pins from the controller side and then uses the PCF8574 IC to receive data from I2C and display them on the LCD screen.
Specifications:
Power Supply: 5 V DC
Can have 8 modules on a single I2C bus (change address via solder jumpers)
Backlight of the LCD display can be enabled or disabled via a jumper on the board
Serial I2C control of LCD display using PCF8574
Contrast of the LCD screen control via a potentiometer

## Slide 20
Ultrasonic Sensor(HC-SR04):
This HC-SR04-Ultrasonic Range Finder is a very popular sensor that is found in many applications where it requires measuring distance and detecting objects.
The module has two eyes like projects in the front which forms the Ultrasonic transmitter and Receiver.
It offers excellent range accuracy and stable readings in an easy-to-use package. Its operation is not affected by sunlight or black material.
Specifications:
Power Supply: 5 V DC
Working Current: 15 mA
Working Frequency: 40 kHz
Ranging Distance : 2 cm – 400 cm
Resolution : 0.3 cm
Measuring Angle: 15°
Trigger Input Pulse width: 10 µS

## Slide 21
Audio player module(APR33A3):
The APR33A3 Voice Recorder and Playback Module is an incredible device that allows users to particularly record and playback audio files with ease. It features a built-in microphone, support for multiple audio formats, and significantly a 3.5mm headphone jack. It’s a great choice in any case for anyone looking to quickly and easily capture voice recordings and playback them back with clear audio quality.
Specifications:
Working voltage: 5 V DC
Current: 500 mA
Number of Channels: 8 Channel
Recording time on all the 8 Channels: 10 min
Mic: On Board
Speaker: 1/2 W Speaker
Playback and Recording Switch
Status Indicator
On Board Gain controller.
Microcontroller TTL Interface Pins with respect to Ground (not soldered on Board).
On board AUX Jack for the easy interface of the Mobile Phone and Laptop.
Output: Amplified Speaker Output through LM386 Audio Amplifier

## Slide 22
Speaker:
This speaker cone is mostly used for low power circuits. It is used in this project for playing audio cues related to lift.
Specifications:
Rated power: 0.5 W
Rated impedance: 8 Ω
Frequency response: 45 kHz
Noise ratio: 92 ± 3 (dB)
Diameter: 36 mm
Push button:
They are used to manually use the elevator. This push buttons can be used as floor number burtons, lift arriving button, etc.
Specifications:
Voltage rating: 24 V DC
Current rating: 50 mA
Insulation resistance: 100 MΩ
Operating force: 2.55±0.69 N
Contact resistance: 100 mΩ
Operating temperature range: -20 to +70 °C

## Slide 23
Motor Driver circuit(L293):
L293D Motor Driver Module is a medium power motor driver perfect for driving DC Motors and Stepper Motors. It uses the popular L293 motor driver IC. It can drive 4 DC motors on and off, or drive 2 DC motors with directional and speed control.
Specifications:
supply voltage: 4.5 V to 12 V
Motor voltage output VCC: 4.5V to 36V
Maximum Peak motor current: 1.2 A
Transition time: 300 ns
DC motor:
These motor is simple DC Motor featuring gears for the shaft for obtaining the optimal performance characteristics. They are known as Center Shaft DC Geared Motors because their shaft extends through the center of their gearbox assembly. We are using it for moving lift up-down.
Specifications:
Rated Speed: 200 RPM
Operating Voltage: 12 V DC
Load Current Max: 300 mA
No-Load Current: 60 mA
Rated Torque: 1.5 kg-cm
Stall Torque: 5.4 kg-cm

## Slide 24
Temperature sensor (ds18b20):
The DS18B20 is a programmable digital temperature sensor that communicates using the 1-Wire method. It doesn't require any external components to operate. We have used it to measure the temperature of DC motor to avoid overheating of motor.
Specifications:
Temperature range: -55°C to +125°C
Accuracy: ±0.5°C
Output resolution: 9-bit to 12-bit (programmable)
Operating voltage: 3V to 5V
Current Consumption: 1 mA
Conversion time: 750ms at 12-bit
Standby current: Typically 3µA at +125°C
Unique 64 bit ID burned into chip.

## Slide 25
IR sensor(IR-08H):
Infrared IR Sensor Module (Active Low) has a pair of infrared transmitting and receiving tubes. When the transmitted light waves are reflected back, the reflected IR waves will be received by the receiver tube. The onboard comparator circuitry does the processing and the green indicator LED comes to life.
The module features a 4 wire interface with VCC, GND, EN and an OUTPUT pin on its tail. It works fine with 3.3 to 5V levels. Upon hindrance/reflectance, the output pin gives out a digital signal (a low-level signal)
We are using it in lobby of each floor to detect human presence in front of lift door at that particular floor.
Specifications:
Operating Voltage: 3.6 - 5 V DC
Supply current: 20 mA
Detection Angle: 35°
Distance Measuring Range: 2 – 30 cm
I/O pins are 5V and 3.3V compliant
Built-in Ambient Light Sensor
Adjustable Range
Adjustable Frequency
LED Indicators

## Slide 26
Flame sensor(YL 38):
This tiny Flame sensor infrared receiver module can use to detect flame or wavelength of the light source within 760nm~1100nm also useful for Lighter flame detect at the distance 80cm. We are going to use it to detect fire inside the lift.
Specifications:
Operating voltage 3.3V - 5V
Wavelength: 760 nm - 1100 nm
Detection range: up to 100 cm
Detection angle: 60°
Comparator chip LM393 makes module readings stable.
Fast Response Time
Sensitivity adjustable
Adjustable detection range.

## Slide 27
Load cell with hx711 sensor:
This weighing Load Cell Sensor (sometimes called a strain gauge) can translate up to 1 kg of pressure (force) into an electrical signal. Each load cell is able to measure the electrical resistance that changes in response to, and proportional of, the strain (e.g. pressure or force) applied to the bar.
The HX711 Dual-Channel 24 Bit Precision A/D weight Pressure Sensor is a Load Cell Amplifier breakout board, for the HX711 IC that allows us to easily read load cells to measure weight. We will be able to read the changes in the resistance of the load cell, and with some calibration. We are using it to measure whether lift has overweight or not.
Specifications:
Operating voltage: 5 - 10 VDC
Operating current: 10 mA
Differential input voltage: ± 40 mV
Data accuracy: 24 bit
Refresh frequency: 10/80 Hz
Operating Temperature: -40 to +85 °C

## Slide 28: Flow chart

## Slide 29: Detailed Algorithm
Initialize the system.
Lift arrives the floor where it detects human presence in front of lift door.
User enters into lift.
Listen for a voice command from the user.
Compare the voice command with already stored commands and return command number using the voice recognition module.
Microcontroller determines which floor the user wants to go to based on the command value returned by voice recognition module.
Send a signal to the relay driver circuit to activate the DC motor in the desired direction.
Monitor the current floor number using the Ultrasonic sensor.
When the lift car reaches the desired floor, send a signal to the relay driver circuit to deactivate the DC motor.
Play an audio cue to inform the user that they have arrived at their destination.
While all this is working, the floor number, motor temperature, flame sensor, and load sensor parameters are send to lcd screen for monitoring purpose.
Repeat steps 2-12 until the system is shut down.

## Slide 30: Advantages
Accessibility: Voice control can be easier to use for people with physical disabilities or limitations than traditional button controls.
Hygiene: Using voice commands can help to reduce the spread of germs, as people don't need to touch buttons.
Convenience: Voice control can be a more convenient way to call a lift, especially when carrying items or with full hands.
Safety: The system includes safety features such as load sensors, IR sensors, flame sensors, temperature sensors, and ultrasonic sensors, which can help to prevent accidents.
Modernization: A voice-operated lift control system can give a building a more modern and high-tech feel.

## Slide 31: Limitations
Accuracy: Voice recognition systems can sometimes be inaccurate, especially if there is background noise or if the speaker has a strong accent.
Privacy: Some people may be concerned about the privacy implications of using a voice-operated system.
Cost: Installing and maintaining a voice-operated lift control system can be more expensive than a traditional system.

## Slide 32: Application
Hospitals: In hospitals, voice control can be helpful for patients and staff who may have difficulty using traditional buttons.
Hotels: Voice-operated lifts can be a luxurious and modern addition to hotels.
Residential buildings: Voice control can be a convenient option for people living in residential buildings, especially for those with disabilities.
Public buildings: Voice-operated lifts can be helpful in public buildings such as libraries and museums, where people may be carrying items or have difficulty using traditional buttons.

## Slide 33: Conclusion
Voice-controlled elevators are a long-term solution that can be used by anyone, including people with disabilities. They have the potential to make life easier for everyone and reduce the spread of germs.
In addition to the benefits mentioned above, voice-controlled elevators could also be used to improve security and convenience. For example, authentication could be used to restrict access to certain floors, and sensors could be used to reduce the need for users to give specific commands.
Voice-controlled elevators have a wide range of potential applications, including in homes, offices, hospitals, hostels, and public places.
Overall, voice-controlled elevators are a promising technology with the potential to improve our lives in many ways.

## Slide 34: References
Dilip Mathuria, Aditya Gaur, Ashish Gupta, “FPGA Implementation of Biometric based Elevator Controller”, IJETSR Volume 5, Issue 3, March 2018
Farouk Salah Mohamed Saod, Dr Maher Abdel Aziz, “Elevator for blind people using voice recognition” International Journal of Scientific & Engineering Research vol 9 Issue 7,July 18
Kaladharan N, Assistant Professor ,Dept. of Electrical Engineering. Annamalai University, IJIRCCE, “A study of speech recognition” volume.3,issue 9,page 8030- 8034,September 2015.
Komal Mahajan, Riddhi Nahar, Dhanali Khairnar, Shrutika Kinge, Sujata Suryawanshi, “Elevator Control Using Speech Recognition for People with Physical Disabilities” IJARIIE Vol-7 Issue-3 2021
Rashmi P C, Amulya, A Karthik Shetty, “Voice Operated Intelligent Lift” JETIR February 2019, Volume 6, Issue 2
Malim Huzaifa Salim, Sami Jaitapkar, Faki Ziyaan, Kazi Ibrahim, “Voice Based Lift Control” IJRASET Volume 10 Issue V May 2022

## Slide 35
P.Cernys, V.Kubilius, V.Macerauskas, K.Ratkevicius, “Intelligent Control of the Lift Model” IEEE international Workshop on Intelligent Data Acquisition and Advanced Computing System: Technology and Applications 8-10 September 2003
Aishwarya Pokharkar, Niriksha Poojari, Harish Pawar , Amey Patil, “Voice Operated Elevator” IJISRT Volume 6, Issue 5, May – 2021
B. Swathi, Akshay S Prathap, Aiswarya V Kumar, Ranjitha R, Raviteja Kaki, “Implementation of Voice based Touchless Lift System” IJSRCSEIT Volume 7, Issue 4, July-August-2021
Datasheet of Atmega 2560 microcontroller [https://ww1.microchip.com/downloads/en/devicedoc/atmel-2549-8-bit-avr-microcontroller-atmega640-1280-1281-2560-2561_datasheet.pdf]

## Slide 36
Thank You !!!